Saratoga CERT – Cox Division

FRS Quick Setup - (Floureon M-880)

General:

- To communicate, all radios in the group need to be set to the same channel and Interference Eliminator Code (IEC). Saratoga CERT uses channel 11 (see step 3) as the primary FRAS communication channel. Saratoga CERT uses channels 10 and 12 as alternate communication channels. Cox Division does NOT use the IEC (see step 4)

- To talk, listen first to determine if someone else is talking. Do NOT interrupt, unless you have an emergency. If the channel is not in use, push the Push-to-Talk (PTT) key. Note that PTT means “push to talk,” NOT “push to think.” Think about what you want to say BEFORE you push the PTT. Hold the radio 2-3 inches from your mouth and speak normally. Don’t yell; it makes things worse! When you finish talking release the PTT and listen.

- The battery icon (upper left of the display) shows the battery charge level, from full to empty. When the battery is near empty, the radio will chirp when the PTT key is released. Remove the batteries when you will be storing the radio for an extended time. [Recommendation: keep the batteries OUT of the radio, but nearby so they can be inserted quickly. Keep a spare set of batteries with your radio. You will NOT lose your channel set with the batteries out. Recommendation: Consider using lithium rather than alkaline batteries. For example, Energizer advertises its Lithium batteries as having a having a 20-year shelf life. Lithium batteries are also much less likely to leak, unlike alkaline batteries, which often leak a corrosive residue. Lithium batteries also produce more power for a longer period of time.]

- For more information, see the M-880 manual at https://fccid.io/2ACVFM-880/User-Manual/User-manual-3401315.

1.  Turn Power on/off:

Press and hold Power/Scan key (left side of face of radio)

2.  Increase/decrease volume:

Press the Up/Down key on face of radio. Volume ranges between 1-16.

3.  Set the channel:

With the radio on, press Menu (center key on face of radio); the current channel flashes.

Press the Up/Down key to change the channel.

Press Push to Talk (PTT) key (left side of radio) to save the channel setting.

4.  Set the Interference Eliminator Code (IEC) to 0:

If your radio has an IOC other than “0” change it to “0.” To do this, with the radio on, press the Menu key until IEC flashes on the right side of the screen (should be the 2nd press of Menu).

Press the Up/Down key until the IEC flashes “00.”

Press PTT to save the IEC setting.

5.  To set the transmit power level (low or high):

With the radio on, press the Menu key until “HI” or “LO” flashes (should be the 7th press of Menu).

Press the Up/Down key until the desired power level flashes.

Press PTT to save the power setting.

6.  To lock/unlock the keypad:

Press and hold the Menu key for three seconds until the lock icon appears/disappears in the top/middle of the display.

[Recommendation: lock your keypad after setting the channel and IEC. This will avoid the problem of inadvertently changing your settings.]

.

Prepared for Saratoga CERT, Cox Division

Prepared by: Peter Melhus – AA6PM

peterjmelhus@gmail.com

Revised Feb 7, 2019